Tutorial Microcontrolador PIC.

Tercera parte.

En la parte anterior vimos como inicializar un PIC, ahora, usando esa información haremos un pequeño programa el cual solo encenderá un LED según el interruptor que se presione.

Lo primero es visualizar lo que queremos,  (ordenar nuestro pines de entrada y salida por ejemplo) y según eso empezar a trabajar.

Figura 3: Circuito a implementar.

Según el circuito anterior, vemos que el puerto A lo usaremos como entrada y el puerto B como salida, a los cuales hemos conectado LED'S para poder ver los resultados.

El puerto A está conectado directamente a la alimentación con lo cual sabemos que normalmente tiene una entrada de +5 V ( 1 lógico) y al activarse el interruptor tendremos un 0 lógico.

Nota: Es muy importante que todos los pines de entrada queden bien definidos si están en un nivel alto o bajo por que de lo contrario el PIC entrará en un estado de incertidumbre y no trabajará de manera correcta. 
            Los pines de salida, no es necesario que se conecten si no los vamos a usar.

Comenzando con el programa.

Como vimos anteriormente, para abrir una nueva ventana de programación pinchamos en la ventana FILE y le damos a la opción NEW, luego debemos inicializar nuestro PIC, en este caso será:

; **************************************** ; * Ejemplo tutorial PIC * ; * Este programa enciende un led dependiendo * ; * de que interruptor sea activado * ; **************************************** list p=16f84 #include p16f84.inc port_a equ 5 port_b equ 6 trisb equ 86 trisa equ 85 retard equ 11 ;RETARDO estado equ 3 clrf estado clrf port_a bsf estado,5 ;selección del banco 1 movlw 0x1f movwf port_a ;define RA0 como entrada clrf port_b movlw 0x00 movwf port_b ;define puerto B como salida bcf estado,5 clrf port_a clrf port_b

Luego podemos hacer que vaya preguntando a cada pin de entrada, recordemos que segun nuestro circuito los pines están normalmente en un nivel alto, y en nuestro caso si este esta en un nivel alto hacemos que testee el siguiente, de lo contrario lo mandamos a un subrutina donde encendemos el LED correspondiente.

Para esto usamos la instrucción btfss (Bit Test F, Skip if Set), es decir, testea el bit f y salta (skip) si esta en un nivel alto (set), el salto se refiere a que la siguiente instrucción no la considera y salta hasta la subsiguiente.

Al empezar un programa, marcamos el inicio de un bloque, en este caso lo llamaremos "inicio", que original no.

inicio btfss port_a,0 ;si el bit 0 del puerto a esta en nivel alto se salta una instrucción call enci0 call retardo btfss port_a,1 ;si el bit 1 del puerto a esta en nivel alto se salta una instrucción call enci1 call retardo btfss port_a,2 ;si el bit 2 del puerto a esta en nivel alto se salta una instrucción call enci2 call retardo btfss port_a,3 ;si el bit 3 del puerto a esta en nivel alto se salta una instrucción call enci3 call retardo btfss port_a,4 ;si el bit 4 del puerto a esta en nivel alto se salta una instrucción call enci4 call retardo goto inicio

En la primera línea, como dice el comentario adjunto, testea el bit 0 del puerto a, si este esta en un nivel alto entonces el programa se salta una instrucción llegando a la instrucción call (llamar) la cual llama  a una subrrutina llamada retardo, de lo contrario, si está en un nivel bajo el programa considera la siguiente instrucción y ejecuta la instrucción call    enci0, en la cual se activa el pin 0 del puerto b que es el puerto se salida.

El resto del programa:

enci0 movlw 0x00 movwf port_b call retar2 movlw B'01' movwf port_b return enci1 movlw 0x00 movwf port_b call retar2 movlw B'10' movwf port_b return enci2 movlw 0x00 movwf port_b call retar2 movlw B'100' movwf port_b return enci3 movlw 0x00 movwf port_b call retar2 movlw B'1000' movwf port_b return enci4 movlw 0x00 movwf port_b call retar2 movlw B'10000' movwf port_b return retardo movlw 0x96 movwf retard reta3 decfsz retard,1 goto reta3 return end

|  |  | En la primera línea lo que hacemos es cargar un cero en el acumulador: movlw 0x00 (MOVe Literal to W) y luego la información que tiene el acumulador (W) la movemos la puerto b: movwf port_b (MOVe W to F), con esto nos aseguramos el todos los LED's del puerto b están apagados. |
| --- | --- | --- |
|  |  | En la tercera línea llamamos un retardo, lo cual siempre es bueno hacer para evitar que el pic colapse, este retardo esta casi al finál del programa y el mecanismo de trabajo es muy parecido al anterior: |

1.- Mover el literal 96 (Hexadecimal) en el acumulador,  en otras palabras cargar un 96 en el acumulador.

2.- Mover el contenido del acumulador al registro retard, el cual fue definido al comienzo de programa y ubicado en la posición 11 en la memoria del pic, ahora el registro retard tiene cargado un 96.

3.- Decrementar en una unidad el registro retard y el valor resultante se guarda en el mismo registro y cuando el valor de este sea cero, saltar una línea en el programa, con lo cual caerá en la instrucción return con lo cual vuelve a la posición desde donde se llamo a la subrutina.   decfsz      f,d (DECrement F, Skip if Zero) (decrementa el registro indicado y salta si es cero) si el valor de "d" es cero entonces el resultado se guarda en el acumulador, si este valor en cambio es uno entonces el valor se almacena en el mismo registro.

4.- Luego va al bloque de nombre "reta 3" con lo cual se volverá a decrementar el registro, esto lo hará durante 96 veces hexadecimales, es decir, 150 veces.

|  |  | Al volver a la 4ta linea de este bloque movlw B'01' hacemos algo muy parecido al paso anterior, sólo que ahora cargo un 1 binario en el acumulador y luego movemos esta información al puerto b, con lo cual tendremos en la salida del puerto b un 00001 considerando que se cuenta desde RB4 hasta RB0 por lo tanto se enciende el LED correspondiente al pin 0 del puerto b. |
| --- | --- | --- |

De esto deducimos que si queremos encender por ejemplo el pin 3 del puerto b, debemos cargar el acumulador con un B'1000' para luego pasar esta información al puerto b.

Otra alternativa seria: movlw   0x08 ya que 08h = 1000b.

Finalmente debemos guardar este programa, para esto pinchamos en la opcion File y luego en Save As y elegimos el directorio y un nombre, en este caso le pondremos ejemplo.asm

Figura 4

Pincha aqui para bajar el programa en formato ASM

En la siguiente parte veremos como compilar este programa y detectar los errores de programación.

# PIC Tutorial Two - Switches

For the first parts of this tutorial you require the Main Board and the Switch Board, the later parts will also use the LED Board, as written the tutorials use the Switch Board on PortA and the LED Board on PortB. Download zipped tutorial files.

Tutorial 2.1 - requires Main Board and Switch Board.

This simple program turns the corresponding LED on, when the button opposite it is pressed, extinguishing all other LED's.

;Tutorial 2.1 - Nigel Goodwin 2002

LIST	p=16F628		;tell assembler what chip we are using

include "P16F628.inc"		;include the defaults for the chip

__config 0x3D18			;sets the configuration settings (oscillator type etc.)

LEDPORT	Equ	PORTA			;set constant LEDPORT = 'PORTA'

SWPORT	Equ	PORTA			;set constant SWPORT = 'PORTA'

LEDTRIS	Equ	TRISA			;set constant for TRIS register

SW1	Equ	7			;set constants for the switches

SW2	Equ	6

SW3	Equ	5

SW4	Equ	4

LED1	Equ	3			;and for the LED's

LED2	Equ	2

LED3	Equ	1

LED4	Equ	0

;end of defines

org	0x0000			;org sets the origin, 0x0000 for the 16F628,

;this is where the program starts running

movlw	0x07

movwf	CMCON			;turn comparators off (make it like a 16F84)

bsf 	STATUS,		RP0	;select bank 1

movlw 	b'11110000'		;set PortA 4 inputs, 4 outputs

movwf 	LEDTRIS

bcf	STATUS,		RP0	;select bank 0

clrf	LEDPORT			;set all outputs low

Loop	btfss	SWPORT,	SW1

call	Switch1

btfss	SWPORT,	SW2

call	Switch2

btfss	SWPORT,	SW3

call	Switch3

btfss	SWPORT,	SW4

call	Switch4

goto	Loop

Switch1	clrf	LEDPORT			;turn all LED's off

bsf	SWPORT,	LED1		;turn LED1 on

retlw	0x00

Switch2	clrf	LEDPORT			;turn all LED's off

bsf	SWPORT,	LED2		;turn LED2 on

retlw	0x00

Switch3	clrf	LEDPORT			;turn all LED's off

bsf	SWPORT,	LED3		;turn LED3 on

retlw	0x00

Switch4	clrf	LEDPORT			;turn all LED's off

bsf	SWPORT,	LED4		;turn LED4 on

retlw	0x00

end

As with the previous tutorials we first set things up, then the main program runs in a loop, the first thing the loop does is check switch SW1 with the 'btfss SWPORT, SW1' line, if the switch isn't pressed the input line is held high by the 10K pull-up resistor and it skips the next line. This takes it to the 'btfss SWPORT, SW2' line, where SW2 is similarly checked - this continues down checking all the switches and then loops back and checks them again. If a key is pressed, the relevant 'btfss' doesn't skip the next line, but instead calls a sub-routine to process the key press, each switch has it's own sub-routine. These sub-routines are very simple, they first 'clrf' the output port, turning all LED's off, and then use 'bsf' to turn on the corresponding LED, next the sub-routine exits via the 'retlw' instruction. As the switch is likely to be still held down, the same routine will be run again (and again, and again!) until you release the key, however for this simple application that isn't a problem and you can't even tell it's happening.

Tutorial 2.2 - requires Main Board and Switch Board.

This program toggles the corresponding LED on and off, when the button opposite it is pressed. It introduces the concept of 'de-bouncing' - a switch doesn't close immediately, it 'bounces' a little before it settles, this causes a series of fast keypresses which can cause chaos in operating a device.

;Tutorial 2.2 - Nigel Goodwin 2002

LIST	p=16F628		;tell assembler what chip we are using

include "P16F628.inc"		;include the defaults for the chip

__config 0x3D18			;sets the configuration settings (oscillator type etc.)

cblock 	0x20 			;start of general purpose registers

count1 			;used in delay routine

counta 			;used in delay routine

countb 			;used in delay routine

endc

LEDPORT	Equ	PORTA			;set constant LEDPORT = 'PORTA'

SWPORT	Equ	PORTA			;set constant SWPORT = 'PORTA'

LEDTRIS	Equ	TRISA			;set constant for TRIS register

SW1	Equ	7			;set constants for the switches

SW2	Equ	6

SW3	Equ	5

SW4	Equ	4

LED1	Equ	3			;and for the LED's

LED2	Equ	2

LED3	Equ	1

LED4	Equ	0

SWDel	Set	Del50			;set the de-bounce delay (has to use 'Set' and not 'Equ')

;end of defines

org	0x0000			;org sets the origin, 0x0000 for the 16F628,

;this is where the program starts running

movlw	0x07

movwf	CMCON			;turn comparators off (make it like a 16F84)

bsf 	STATUS,		RP0	;select bank 1

movlw 	b'11110000'		;set PortA 4 inputs, 4 outputs

movwf 	LEDTRIS

bcf	STATUS,		RP0	;select bank 0

clrf	LEDPORT			;set all outputs low

Loop	btfss	SWPORT,	SW1

call	Switch1

btfss	SWPORT,	SW2

call	Switch2

btfss	SWPORT,	SW3

call	Switch3

btfss	SWPORT,	SW4

call	Switch4

goto	Loop

Switch1	call	SWDel			;give switch time to stop bouncing

btfsc	SWPORT,	SW1		;check it's still pressed

retlw	0x00			;return is not

btfss	SWPORT,	LED1		;see if LED1 is already lit

goto	LED1ON

goto	LED1OFF

LED1ON	bsf	LEDPORT,	LED1	;turn LED1 on

call	SWDel

btfsc	SWPORT,	SW1		;wait until button is released

retlw	0x00

goto	LED1ON

LED1OFF	bcf	LEDPORT,	LED1	;turn LED1 on

call	SWDel

btfsc	SWPORT,	SW1		;wait until button is released

retlw	0x00

goto	LED1OFF

Switch2	call	SWDel			;give switch time to stop bouncing

btfsc	SWPORT,	SW2		;check it's still pressed

retlw	0x00			;return is not

btfss	SWPORT,	LED2		;see if LED2 is already lit

goto	LED2ON

goto	LED2OFF

LED2ON	bsf	LEDPORT,	LED2	;turn LED2 on

call	SWDel

btfsc	SWPORT,	SW2		;wait until button is released

retlw	0x00

goto	LED2ON

LED2OFF	bcf	LEDPORT,	LED2	;turn LED2 on

call	SWDel

btfsc	SWPORT,	SW2		;wait until button is released

retlw	0x00

goto	LED2OFF

Switch3	call	SWDel			;give switch time to stop bouncing

btfsc	SWPORT,	SW3		;check it's still pressed

retlw	0x00			;return is not

btfss	SWPORT,	LED3		;see if LED3 is already lit

goto	LED3ON

goto	LED3OFF

LED3ON	bsf	LEDPORT,	LED3	;turn LED3 on

call	SWDel

btfsc	SWPORT,	SW3		;wait until button is released

retlw	0x00

goto	LED3ON

LED3OFF	bcf	LEDPORT,	LED3	;turn LED3 on

call	SWDel

btfsc	SWPORT,	SW3		;wait until button is released

retlw	0x00

goto	LED3OFF

Switch4	call	SWDel			;give switch time to stop bouncing

btfsc	SWPORT,	SW4		;check it's still pressed

retlw	0x00			;return is not

btfss	SWPORT,	LED4		;see if LED4 is already lit

goto	LED4ON

goto	LED4OFF

LED4ON	bsf	LEDPORT,	LED4	;turn LED4 on

call	SWDel

btfsc	SWPORT,	SW4		;wait until button is released

retlw	0x00

goto	LED4ON

LED4OFF	bcf	LEDPORT,	LED4	;turn LED4 on

call	SWDel

btfsc	SWPORT,	SW4		;wait until button is released

retlw	0x00

goto	LED4OFF

;modified Delay routine, direct calls for specified times

;or load W and call Delay for a custom time.

Del0	retlw	0x00			;delay 0mS - return immediately

Del1	movlw	d'1'			;delay 1mS

goto	Delay

Del5	movlw	d'5'			;delay 5mS

goto	Delay

Del10	movlw	d'10'			;delay 10mS

goto	Delay

Del20	movlw	d'20'			;delay 20mS

goto	Delay

Del50	movlw	d'50'			;delay 50mS

goto	Delay

Del100	movlw	d'100'			;delay 100mS

goto	Delay

Del250	movlw	d'250'			;delay 250 ms

Delay	movwf	count1

d1	movlw	0xC7			;delay 1mS

movwf	counta

movlw	0x01

movwf	countb

Delay_0

decfsz	counta, f

goto	$+2

decfsz	countb, f

goto	Delay_0

decfsz	count1	,f

goto	d1

retlw	0x00

end

In order to de-bounce the keypresses we delay for a short time, then check that the button is still pressed, the time delay is set by the variable SWDel, which is defined as Del50 in the defines section at the start of the program. I've extended the Delay routine to provide a selection of different delays (from 0mS to 250mS), called by simple 'call' instructions, the Delay routine itself can also be called directly - simply load the required delay into the W register and 'call Delay'. We then check to see if the corresponding LED is lit, with 'btfss SWPORT, LEDx', and jump to either 'LEDxON' or 'LEDxOFF', these routines are almost identical, the only difference being that the first turns the LED on, and the second turns it off. They first switch the LED, on or off, depending on which routine it is, and then delay again (calling SWDel as before), next they check to see if the button is still pressed, looping back around if it is. Once the key has been released the routine exits via the usual 'retlw' and returns to waiting for a keypress. I've used the variable SWDel (and provided the various delay times) so that you can easily try the effect of different delay times - in particular try setting SWDel to Del0, and see how the button pressing isn't reliable, you will probably find one of the buttons is worse than the others - particularly if you use old switches, wear makes them bounce more.

Tutorial 2.3 - requires Main Board, Switch Board, and LED Board.

Now for a more realistic example - this combines Tutorial 2.1 with Tutorial 1.9, the result is an LED sequencing program with four different patterns, selected by the four keys, with the key selected indicated by the corresponding LED.

;Tutorial 2.3 - Nigel Goodwin 2002

LIST	p=16F628		;tell assembler what chip we are using

include "P16F628.inc"		;include the defaults for the chip

__config 0x3D18			;sets the configuration settings (oscillator type etc.)

cblock 	0x20 			;start of general purpose registers

count			;used in table read routine

count1 			;used in delay routine

counta 			;used in delay routine

countb 			;used in delay routine

endc

LEDPORT	Equ	PORTB			;set constant LEDPORT = 'PORTB'

LEDTRIS	Equ	TRISB			;set constant for TRIS register

SWPORT	Equ	PORTA

SWTRIS	Equ	TRISA

SW1	Equ	7			;set constants for the switches

SW2	Equ	6

SW3	Equ	5

SW4	Equ	4

LED1	Equ	3			;and for the LED's

LED2	Equ	2

LED3	Equ	1

LED4	Equ	0

org	0x0000			;org sets the origin, 0x0000 for the 16F628,

;this is where the program starts running

movlw	0x07

movwf	CMCON			;turn comparators off (make it like a 16F84)

bsf 	STATUS,		RP0	;select bank 1

movlw 	b'00000000'		;set PortB all outputs

movwf 	LEDTRIS

movlw 	b'11110000'		;set PortA 4 inputs, 4 outputs

movwf 	SWTRIS

bcf	STATUS,		RP0	;select bank 0

clrf	LEDPORT			;set all outputs low

clrf	SWPORT

bsf	SWPORT,	LED1		;set initial pattern

Start	clrf	count			;set counter register to zero

Read	movf	count, w		;put counter value in W

btfsc	SWPORT,	LED1		;check which LED is lit

call	Table1			;and read the associated table

btfsc	SWPORT,	LED2

call	Table2

btfsc	SWPORT,	LED3

call	Table3

btfsc	SWPORT,	LED4

call	Table4

movwf	LEDPORT

call	Delay

incf	count,	w

xorlw	d'14'			;check for last (14th) entry

btfsc	STATUS,	Z

goto	Start			;if start from beginning

incf	count,	f		;else do next

goto	Read

Table1	ADDWF   PCL, f			;data table for bit pattern

retlw	b'10000000'

retlw   b'01000000'

retlw   b'00100000'

retlw   b'00010000'

retlw   b'00001000'

retlw   b'00000100'

retlw   b'00000010'

retlw   b'00000001'

retlw   b'00000010'

retlw   b'00000100'

retlw   b'00001000'

retlw   b'00010000'

retlw   b'00100000'

retlw   b'01000000'

Table2	ADDWF   PCL, f			;data table for bit pattern

retlw	b'11000000'

retlw   b'01100000'

retlw   b'00110000'

retlw   b'00011000'

retlw   b'00001100'

retlw   b'00000110'

retlw   b'00000011'

retlw   b'00000011'

retlw   b'00000110'

retlw   b'00001100'

retlw   b'00011000'

retlw   b'00110000'

retlw   b'01100000'

retlw   b'11000000'

Table3	ADDWF   PCL, f			;data table for bit pattern

retlw	b'01111111'

retlw   b'10111111'

retlw   b'11011111'

retlw   b'11101111'

retlw   b'11110111'

retlw   b'11111011'

retlw   b'11111101'

retlw   b'11111110'

retlw   b'11111101'

retlw   b'11111011'

retlw   b'11110111'

retlw   b'11101111'

retlw   b'11011111'

retlw   b'10111111'

Table4	ADDWF   PCL, f			;data table for bit pattern

retlw	b'00111111'

retlw   b'10011111'

retlw   b'11001111'

retlw   b'11100111'

retlw   b'11110011'

retlw   b'11111001'

retlw   b'11111100'

retlw   b'11111100'

retlw   b'11111001'

retlw   b'11110011'

retlw   b'11100111'

retlw   b'11001111'

retlw   b'10011111'

retlw   b'00111111'

ChkKeys	btfss	SWPORT,	SW1

call	Switch1

btfss	SWPORT,	SW2

call	Switch2

btfss	SWPORT,	SW3

call	Switch3

btfss	SWPORT,	SW4

call	Switch4

retlw	0x00

Switch1	clrf	SWPORT			;turn all LED's off

bsf	SWPORT,	LED1		;turn LED1 on

retlw	0x00

Switch2	clrf	SWPORT			;turn all LED's off

bsf	SWPORT,	LED2		;turn LED2 on

retlw	0x00

Switch3	clrf	SWPORT			;turn all LED's off

bsf	SWPORT,	LED3		;turn LED3 on

retlw	0x00

Switch4	clrf	SWPORT			;turn all LED's off

bsf	SWPORT,	LED4		;turn LED4 on

retlw	0x00

Delay	movlw	d'250'			;delay 250 ms (4 MHz clock)

movwf	count1

d1	call 	ChkKeys 		;check the keys

movlw	0xC7			;delay 1mS

movwf	counta

movlw	0x01

movwf	countb

Delay_0

decfsz	counta, f

goto	$+2

decfsz	countb, f

goto	Delay_0

decfsz	count1	,f

goto	d1

retlw	0x00

end

The main differences here are in the Delay routine, which now has a call to check the keys every milli-second, and the main loop, where it selects one of four tables to read, depending on the settings of flag bits which are set according to which key was last pressed.

Tutorial 2.4 - requires Main Board, Switch Board, and LED Board.

Very similar to the last tutorial, except this one combines Tutorials 2.2 and 2.3 with Tutorial 1.9, the result is an LED sequencing program with three different patterns, selected by three of the keys, with the key selected indicated by the corresponding LED - the difference comes with the fourth switch, this selects slow or fast speeds, with the fast speed being indicated by a toggled LED.

;Tutorial 2.4 - Nigel Goodwin 2002

LIST	p=16F628		;tell assembler what chip we are using

include "P16F628.inc"		;include the defaults for the chip

__config 0x3D18			;sets the configuration settings (oscillator type etc.)

cblock 	0x20 			;start of general purpose registers

count			;used in table read routine

count1 			;used in delay routine

count2 			;used in delay routine

counta 			;used in delay routine

countb

countc

countd

speed

endc

LEDPORT	Equ	PORTB			;set constant LEDPORT = 'PORTB'

LEDTRIS	Equ	TRISB			;set constant for TRIS register

SWPORT	Equ	PORTA

SWTRIS	Equ	TRISA

SW1	Equ	7			;set constants for the switches

SW2	Equ	6

SW3	Equ	5

SW4	Equ	4

LED1	Equ	3			;and for the LED's

LED2	Equ	2

LED3	Equ	1

LED4	Equ	0

SWDel	Set	Del50

org	0x0000			;org sets the origin, 0x0000 for the 16F628,

;this is where the program starts running

movlw	0x07

movwf	CMCON			;turn comparators off (make it like a 16F84)

bsf 	STATUS,		RP0	;select bank 1

movlw 	b'00000000'		;set PortB all outputs

movwf 	LEDTRIS

movlw 	b'11110000'		;set PortA 4 inputs, 4 outputs

movwf 	SWTRIS

bcf	STATUS,		RP0	;select bank 0

clrf	LEDPORT			;set all outputs low

clrf	SWPORT			;make sure all LED's are off

bsf	SWPORT,	LED1		;and turn initial LED on

movlw	d'250'

movwf	speed			;set initial speed

Start	clrf	count			;set counter register to zero

Read	movf	count, w		;put counter value in W

btfsc	SWPORT,	LED1		;check which LED is on

call	Table1			;and call the associated table

btfsc	SWPORT,	LED2

call	Table2

btfsc	SWPORT,	LED3

call	Table3

movwf	LEDPORT

call	DelVar

incf	count,	w

xorlw	d'14'			;check for last (14th) entry

btfsc	STATUS,	Z

goto	Start			;if start from beginning

incf	count,	f		;else do next

goto	Read

Table1	ADDWF   PCL, f			;data table for bit pattern

retlw	b'10000000'

retlw   b'01000000'

retlw   b'00100000'

retlw   b'00010000'

retlw   b'00001000'

retlw   b'00000100'

retlw   b'00000010'

retlw   b'00000001'

retlw   b'00000010'

retlw   b'00000100'

retlw   b'00001000'

retlw   b'00010000'

retlw   b'00100000'

retlw   b'01000000'

Table2	ADDWF   PCL, f			;data table for bit pattern

retlw	b'11000000'

retlw   b'01100000'

retlw   b'00110000'

retlw   b'00011000'

retlw   b'00001100'

retlw   b'00000110'

retlw   b'00000011'

retlw   b'00000011'

retlw   b'00000110'

retlw   b'00001100'

retlw   b'00011000'

retlw   b'00110000'

retlw   b'01100000'

retlw   b'11000000'

Table3	ADDWF   PCL, f			;data table for bit pattern

retlw	b'01111111'

retlw   b'10111111'

retlw   b'11011111'

retlw   b'11101111'

retlw   b'11110111'

retlw   b'11111011'

retlw   b'11111101'

retlw   b'11111110'

retlw   b'11111101'

retlw   b'11111011'

retlw   b'11110111'

retlw   b'11101111'

retlw   b'11011111'

retlw   b'10111111'

ChkKeys	btfss	SWPORT,	SW1

call	Switch1

btfss	SWPORT,	SW2

call	Switch2

btfss	SWPORT,	SW3

call	Switch3

btfss	SWPORT,	SW4

call	Switch4

retlw	0x00

Switch1	bcf	SWPORT,	LED2		;turn unselected LED's off

bcf	SWPORT,	LED3		;turn unselected LED's off

bsf	SWPORT,	LED1		;turn LED1 on

retlw	0x00

Switch2	bcf	SWPORT,	LED1		;turn unselected LED's off

bcf	SWPORT,	LED3		;turn unselected LED's off

bsf	SWPORT,	LED2		;turn LED2 on

retlw	0x00

Switch3	bcf	SWPORT,	LED1		;turn unselected LED's off

bcf	SWPORT,	LED2		;turn unselected LED's off

bsf	SWPORT,	LED3		;turn LED3 on

retlw	0x00

Switch4	call	SWDel			;give switch time to stop bouncing

btfsc	SWPORT,	SW4		;check it's still pressed

retlw	0x00			;return is not

btfss	SWPORT,	LED4		;see if LED4 is already lit

goto	FASTON

goto	FASTOFF

FASTON	bsf	SWPORT,	LED4		;turn LED4 on

movlw	d'80'

movwf	speed			;set fast speed

call	SWDel

btfsc	SWPORT,	SW4		;wait until button is released

retlw	0x00

goto	FASTON

FASTOFF	bcf	SWPORT,	LED4		;turn LED4 on

movlw	d'250'

movwf	speed			;set slow speed

call	SWDel

btfsc	SWPORT,	SW4		;wait until button is released

retlw	0x00

goto	FASTOFF

DelVar	movfw	speed			;delay set by Speed

movwf	count1

d1	call 	ChkKeys 		;check the keys

movlw	0xC7			;delay 1mS

movwf	counta

movlw	0x01

movwf	countb

Delay_0

decfsz	counta, f

goto	$+2

decfsz	countb, f

goto	Delay_0

decfsz	count1	,f

goto	d1

retlw	0x00

;use separate delay routines, as Del50 is called from ChkKeys

;which is called from within DelVar

Del50	movlw	d'50'			;delay 50mS

movwf	count2

d3	movlw	0xC7			;delay 1mS

movwf	countc

movlw	0x01

movwf	countd

Delay_1

decfsz	countc, f

goto	$+2

decfsz	countd, f

goto	Delay_1

decfsz	count2	,f

goto	d3

retlw	0x00

end